Data Conversion of Data Transmission for Gigabit Ethernet (1000BASE-X):

Bit Conversion (Engineering Data Conversion) for 1000BASE-X:
0.9313 Gib/s = 953.6743 Mib/s = 976,562.5 Kib/s
Byte Conversion (Modern Data Conversion) for 1000BASE-X:
- 1 Gb/s = 1,000 Mb/s = 1,000,000 Kb/s
- 0.125 GB/s = 125 MB/s = 125,000 KB/s

List of Interface Rated Speed Source:
 https://en.wikipedia.org/wiki/List_of_interface_bit_rates#Main_buses

Note: The speed of data transfer on a USB interface is affected by the amount of data that can be transferred. USB interfaces sometimes reach their limit or experience a drop in speed. This is due to overhead on USB devices. Overhead can increase data transmission by around 5% to 8% and can also cause the speed to drop by about 10%.

USB 2.0 Standard:
PC / Server < - - - - - USB 2.0 - - - - - - > Gigabit Ethernet
- Max Performance Data Transmission / Signaling Rate:
- USB 2.0 Standard Limits
- 0.447 Gib/s = 457.7637 Mib/s = 468,750 Kib/s on USB 2.0 Standard (Max Limit)
- 0.48 Gb/s = 480 Mb/s = 480,000 Kb/s
- 0.06 GB/s = 60 MB/s = 60,000 KB/s
- The Max Speed USB 2.0 = 60 MB/s
    - Gigabit Ethernet Standard Limits
      - 0.9313 Gib/s = 953.6743 Mib/s = 976,562.5 Kib/s on Gigabit Ethernet Standard
      - 1 Gb/s = 1,000 Mb/s = 1,000,000 Kb/s
      - 0.125 GB/s = 125 MB/s = 125,000 KB/s
      - The Max Speed Gigabit Ethernet = 125 MB/s
Bottleneck in Data Transmission / Signaling Rate: USB 2.0 Standard
Due to the max speed being 60 MB/s with USB 2.0 Standard compared to Gigabit Ethernet being 125 MB/s.
It will leave 65 MB/s not being used to the maximum limit for Gigabit Ethernet Standard.

USB 3.0 Standard:
PC / Server < - - - - - USB 3.0 - - - - - - > Gigabit Ethernet
- Max Performance Data Transmission / Signaling Rate:
- USB 3.0 Standard Limits
- 4.6566 Gib/s = 4,768.3716 Mib/s = 4,882,812.5 Kib/s on USB 3.0 Standard (Max Limit)
- 5 Gb/s = 5,000 Mb/s = 5,000,000 Kb/s
- 0.625 GB/s = 625 MB/s = 625,000 KB/s
- The Max Speed USB 3.0 = 625 MB/s
- Gigabit Ethernet Standard Limits
      - 0.9313 Gib/s = 953.6743 Mib/s = 976,562.5 Kib/s on Gigabit Ethernet Standard (Max Limit)
      - 1 Gb/s = 1,000 Mb/s = 1,000,000 Kb/s
      - 0.125 GB/s = 125 MB/s = 125,000 KB/s
      - The Max Speed Gigabit Ethernet = 125 MB/s
Bottleneck in Data Transmission / Signaling Rate: Gigabit Ethernet Standard
- Due to the fact that the max speed will be 125 MB/s for Gigabit Ethernet compared to USB 3.0 being 625 MB/s.
- It will leave 500 MB/s not being used to reach the maximum limit for USB 3.0 Standard.

USB 3.1 Standard:
PC / Server < - - - - - USB 3.1 - - - - - - > Gigabit Ethernet
- Max Performance Data Transmission / Signaling Rate:
- USB 3.1 Standard Limits
- 9.3132 Gib/s = 9,536.7432 Mib/s = 9,765,625 Kib/s on USB 3.1 Standard (Max Limit)
- 10 Gb/s = 10,000 Mb/s = 10,000,000 Kb/s
- 1.25 GB/s = 1,250 MB/s = 1,250,000 KB/s
- The Max Speed USB 3.1 = 1,250 MB/s
- Gigabit Ethernet Standard Limits
- 0.9313 Gib/s = 953.6743 Mib/s = 976,562.5 Kib/s on Gigabit Ethernet Standard (Max Limit)
- 1 Gb/s = 1,000 Mb/s = 1,000,000 Kb/s
- 0.125 GB/s = 125 MB/s = 125,000 KB/s
- The Max Speed Gigabit Ethernet = 125 MB/s
Bottleneck in Data Transmission / Signaling Rate: Gigabit Ethernet Standard
- Due to the fact that the maximum speed will be 125 MB/s for Gigabit Ethernet compared to USB 3.1 being 1,250 MB/s.
- It will leave 1,125 MB/s not being used to the maximum limit for USB 3.1 Standard.

USB 3.2 Standard:
PC / Server < - - - - - USB 3.2 - - - - - - > Gigabit Ethernet
- Max Performance Data Transmission / Signaling Rate:
- USB 3.2 Standard Limits
- 18.6265 Gib/s = 19,073.4863 Mib/s = 19,531,250 Kib/s on USB 3.2 Standard (Max Limit)
- 20 Gb/s = 20,000 Mb/s = 20,000,000 Kb/s
- 2.5 GB/s = 2,500 MB/s = 2,000,000 KB/s
- The Max Speed USB 3.2 = 2,500 MB/s
- Gigabit Ethernet Standard Limits
      - 0.9313 Gib/s = 953.6743 Mib/s = 976,562.5 Kib/s on Gigabit Ethernet Standard (Max Limit)
      - 1 Gb/s = 1,000 Mb/s = 1,000,000 Kb/s
      - 0.125 GB/s = 125 MB/s = 125,000 KB/s
      - The Max Speed Gigabit Ethernet = 125 MB/s
Bottleneck in Data Transmission / Signaling Rate: Gigabit Ethernet Standard
- Due to the fact that the maximum speed will be 125 MB/s for Gigabit Ethernet compared to USB 3.2 being 2,500 MB/s.
- It will leave 2,375 MB/s not being used to the maximum limit for USB 3.2 Standard.

USB 4.0 Standard:
PC / Server < - - - - - USB 4.0 - - - - - - > Gigabit Ethernet
- Max Performance Data Transmission / Signaling Rate:
- USB 4.0 Standard Limits
- 37.2529 Gib/s = 38,176.9727 Mib/s = 39,062,500 Kib/s on USB 4.0 Standard (Max Limit)
- 40 Gb/s = 40,000 Mb/s = 40,000,000 Kb/s
- 5 GB/s = 5,000 MB/s = 5,000,000 KB/s
- The Max Speed USB 4.0 = 5,000 MB/s
- Gigabit Ethernet Standard Limits
- 0.9313 Gib/s = 953.6743 Mib/s = 976,562.5 Kib/s on Gigabit Ethernet Standard (Max Limit)
- 1 Gb/s = 1,000 Mb/s = 1,000,000 Kb/s
- 0.125 GB/s = 125 MB/s = 125,000 KB/s
- The Max Speed Gigabit Ethernet = 125 MB/s
Bottleneck in Data Transmission / Signaling Rate: Gigabit Ethernet Standard
- Due to the fact that the maximum speed will be 125 MB/s for Gigabit Ethernet compared to USB 4.0 being 5,000 MB/s.
- It will leave 4,875 MB/s not being used to the maximum limit for USB 4.0 Standard.

USB 4.0 v2.0 Standard:
PC / Server < - - - - - USB 4.0 v2.0 - - - - - - > Gigabit Ethernet
- Max Performance Data Transmission / Signaling Rate:
- USB 4.0 v2.0 Standard Limits
- 74.5058 Gib/s = 76,293.9453 Mib/s = 78,125,000 Kib/s on USB 4.0 v2.0 Standard (Max Limit)
- 80 Gb/s = 80,000 Mb/s = 80,000,000 Kb/s
- 10 GB/s = 10,000 MB/s = 10,000,000 KB/s
- The Max Speed USB 4.0 v2.0 = 10,000 MB/s
- Gigabit Ethernet Standard Limits
- 0.9313 Gib/s = 953.6743 Mib/s = 976,562.5 Kib/s on Gigabit Ethernet Standard (Max Limit)
- 1 Gb/s = 1,000 Mb/s = 1,000,000 Kb/s
- 0.125 GB/s = 125 MB/s = 125,000 KB/s
- The Max Speed Gigabit Ethernet = 125 MB/s
Bottleneck in Data Transmission / Signaling Rate: Gigabit Ethernet Standard
Due to the fact that the maximum speed will be 125 MB/s for Gigabit Ethernet compared to USB 4.0 v2.0 being 10,000 MB/s.
It will leave 9,875 MB/s not being used to the maximum limit for USB 4.0 v2.0 Standard.